## Slide 1: Smart Home Monitoring System
By Florian Poppinger
Notes: Welcome to the Smart Home Monitoring System presentation. This project utilizes a Raspberry Pi and various IoT technologies to enhance home security and provide real-time environmental monitoring. The objective was to create a responsive system that notifies homeowners of important events and changes in their environment, leveraging real-time data processing and IoT communications.

## Slide 2: Core Technologies and Tools
Raspberry Pi & Sense HAT: Core hardware for data collection and processing.
Camera: For motion detection and security surveillance.
MQTT: Message protocol for efficient real-time communication.
Firebase: Cloud storage for image archiving and retrieval.
Blynk: Interface for real-time interaction and monitoring.
Python: Primary programming language.
Notes: In this project, I've used several key technologies. Firstly, the Raspberry Pi, combined with a Sense HAT, acts as the nerve center, collecting data and controlling other devices. A camera attached to the Raspberry Pi enables real-time security monitoring through motion detection. I use MQTT for efficient message passing between devices, Firebase for storing captured images securely, and Blynk for user interaction, allowing homeowners to see data updates in real-time on their mobile devices. The entire system is programmed in Python.

## Slide 3: System Demonstration
Notes: Let's look at a demonstration of the system. The process begins when motion is detected by the camera, triggering the system to capture an image and environmental data from the Sense HAT. This data, along with the image, is then sent via email to the homeowner for immediate notification. Concurrently, the data is displayed on the Blynk app, providing real-time updates directly to the user's smartphone. This allows for quick reactions and monitoring directly from anywhere in the world.

## Slide 4: Reflection
Problem 1: Issues with MQTT, Blynk connectivity under variable network conditions.
Solution: could implement a more robust connection handling and reconnection strategy.
Problem 2: incorrect Threshold value
Solution: Testing under ideal Circumstances which value would fit better
Problem 3: Managing concurrent data streams efficiently.
Solution: Instead of Threads multiple Terminals Usage may be better
Notes: During the development of this system, I encountered several challenges. One significant issue was maintaining reliable MQTT connectivity, especially in fluctuating network conditions. To address this, I would implement automatic reconnection protocols that help ensure continuous data flow. Another challenge was the incorrect Threshold value I would need some more testing under ideal Circumstances for a better value. Lastly, managing multiple Threads can easy lead to many problems so I could use multiple Terminals instead

## Slide 5: Future Work
Integration of Additional Sensors: Plans to include air quality and noise level sensors for more comprehensive monitoring.
Advanced Data Analysis Features: Implement machine learning algorithms to predict potential security threats or hazardous environmental conditions.
Enhanced User Interface: Develop a more sophisticated web dashboard that offers greater functionality and customization.
Video Features: Enhancing the system by incorporating features such as live streaming.
Notes: Looking ahead, I have several enhancements planned for the system. First, I could integrate additional sensors to monitor air quality and noise levels, creating a more comprehensive environment assessment tool. I could also look into applying machine learning algorithms to predict potential security threats and environmental hazards based on accumulated data for example with a co2 monitoring. A good upgrade would be to enhance the user interface with a more advanced web dashboard that allows for extensive customization and increased functionality, maby a self-made and not blynk . Lastly, I would like to expand the system's video capabilities. This includes adding features such as live streaming, so a user can livestream the camera from his phone.